## Slide 1
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 01/07
A.E.T.H.E.R
Integrity-Aware Visual-Inertial Odometry for a GPS-denied indoor drone
TEAM Rayyan · Ashitha
DEPT 2nd-year · CSE/ECE
SUBMIT 08 Jun 2026 (design)
FINAL 12 Jun 2026 (3-hr)
EVENT Honeywell × RVCE
≤ 3.0 m
IB k=2.45
—— VIO estimate – – ground truth ◯ integrity bound · ● true position
ABSTRACT
“When the camera dies, our drift bound still covers the true position 95%+ of the time — and we know within half a second.”
An open-source, student-scale instantiation of Honeywell's HANA resilient-PNT philosophy — RAIM, for the vision aid.
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 1/7
ILLUSTRATIVE / TARGET — 8 JUN DESIGN PROPOSAL, NOT MEASURED

## Slide 2
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 02/07
The problem, reframed
DP7 is an Assured-PNT problem — not a SLAM exercise
DP7 SPEC
GNSS-denied tunnel/warehouse · drift < 1.5% / 200 m · ROS2 + Gazebo · estimate-vs-GT report · documented ROS2 workspace
“Everyone can plot a trajectory. The unsolved question is — how wrong am I right now, and do I know it in time?”
THE FLOOR IS A FLOOR
Stock stereo-inertial VIO already clears 1.5% in sim (~0.1–0.3% drift). 80–90% of teams hit it. We own the regime where that number quietly breaks — and prove our bound stays honest through it.
Fig. 2 — translational drift vs distance [KITTI seg-RPE]
1.5 % limit (= 3.0 m @ 200 m)
estimate drift
drift %
0
100
200 m
3%
1.5%
0%
PASS band
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 2/7
ILLUSTRATIVE / TARGET — 8 JUN DESIGN PROPOSAL, NOT MEASURED

## Slide 3
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 03/07
Why Honeywell — the wedge
RAIM for the vision aid
IMU = the spine
vision = the aid that BOUNDS INS drift
integrity (RAIM-for-vision) clamps the drift here
Fig. 3 — dead-reckoning @ 8 s vision outage, 1.5 m/s
HG4930 tactical
0.4 m
industrial MEMS ~1.5 mg
1.2 m
consumer ~20 mg
6.3 m
cross-checked to first-principles physics ±20%
“GNSS has RAIM — a live integrity check. Vision aiding has none. We build it.”
HANA Honeywell Alternative Navigation Architecture (Oct 2025) — software, layered, INS + aiding modalities; first release = vision-aided nav. The judges built this.
THE RUBRIC, SELF-SCORED
median “flythrough” team | A.E.T.H.E.R
a trajectory + an ATE number | a live, fault-derived relative integrity bound
“it localizes” | “it knows when it can't be trusted”
clean flythrough | kill-the-camera: bound breathes, trust flips red
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 3/7

## Slide 4
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 04/07
Architecture — five independent ROS2 nodes
graceful by construction · any subset runs
sensor_bridge
stereo · IMU · GT
/sensor_bridge/imu
vio_core
OpenVINS ov_msckf
/ov_msckf/odomimu
NOVEL · the wedge
integrity_monitor
D · NIS · NEES · IB
/nav/integrity_bound
degradation_mgr
R(D) state machine
/nav/trust
health_cockpit
trust HUD · ellipse
/nav/integrity_bound · VioInternals.msg {P, ν_i, S_i, H̃x_i, χ²}
degradation_manager R(D):
NOMINAL
DEGRADED
INERTIAL
RE-ACQUIRE
ANY SUBSET RUNS
Each box is a standalone ROS2 node — a failed module never cascades. Graceful degradation is proven by the graph itself, not promised in prose.
THE LIVE DEMO IS PYTHON
integrity_monitor consumes only what OpenVINS already publishes — pose+covariance on /ov_msckf/odomimu + feature count. No C++ fork on the critical path.
WHERE WE KNOW IN 0.5 s
integrity_monitor is the red node — the layer Honeywell ships and stock VIO lacks. It turns “it localizes” into “it knows when it can't be trusted.”
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 4/7

## Slide 5
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 05/07
The novelty — a live, fault-derived integrity bound
observability-conditioned · multi-class · NEES-validated (relative datum)
OBSERVABILITY INDEX D ∈ [0,1]
Smallest eigenvalue of the whitened visual-information matrix on the motion-degenerate subspace — knows WHICH state direction vision can't see (e.g. scale), not just “few features.”
FAULT-DERIVED, NOT A σ-ELLIPSE
A real fault hypothesis + non-central-χ² detection (the RAIM slope) → a protection level on the segment-RPE quantity DP7 grades. Dual bound: operational k=2.45, DAL-C k=6.74.
THE BOUND IS HONEST
NEES vs ground truth proves the claimed bound actually covers the truth — in nominal AND outage windows. Integrity is meaningless if the bound lies.
LITERATURE GAP — no prior work in the bottom-right cell:
Zhang&Singh (degeneracy) · Hesch/Kottas (OC-EKF) · RAIM (GNSS) · Gupta&Gao (vision integrity = open) → observability-conditioned + scheduler-wired + NEES-validated on ONE pipeline = ours.
k=2.45 · IB ≈ 1.31 m
k_ffd=6.74 · DAL-C
true error ≈ 0.3 m
BOUND LEDGER
operational k=2.45 → 95% containment, the bound we act on
DAL-C k_ffd=6.74 → exceedance 1.39e-10 (scipy)
λ_md=45.0 · T_D=13.82 · IB_assoc ≈ 1.31 m covers true ≈ 0.3 m
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 5/7
ILLUSTRATIVE / TARGET — 8 JUN DESIGN PROPOSAL, NOT MEASURED

## Slide 6
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 06/07
The demo — kill the camera, watch the bound breathe
t=9s
t=18s
t=28s
camera black @ 8 s → bound blooms to ~1.0–1.1 m, chasing & containing the moving truth. TRUTH ∈ BOUND: 100%
0–8 s NOMINAL · drift<1.5%
8 s FAULT · camera black, stock VIO lies
8–9 s TRUST RED <0.5 s · degrade to inertial
9–28 s ellipse BLOOMS, contains truth
28–32 s vision back · re-converge · green
THE NUMBERS
95%+
IB covers true error (held-out)
< 0.5 s
fault detected, trust flips red
0.4 m
drift /8 s · HG4930 [datasheet]
±20%
dead-reckon vs physics check
est-vs-GT · drift < 1.5% (illustrative)
3-RUNG SAFETY LADDER
live → rosbag-replay → backup video. The kill-camera beat is identical on rungs 1–2; the integrity layer runs on EuRoC even if sim wobbles.
“When the camera dies, our drift bound still covers the truth 95%+ of the time — and we know within half a second.”
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 6/7
ILLUSTRATIVE / TARGET — 8 JUN DESIGN PROPOSAL, NOT MEASURED

## Slide 7
TRUTH ∈ BOUND
FLIGHT-TEST REPORT · AE-001 · DP7 · DWG 07/07
Build plan & feasibility — de-risked to a guaranteed floor
2 people · 8–11 Jun build · 12 Jun demo
8 Jun
9 Jun
10 Jun
11 Jun
12 Jun
#1 RISK · Windows → Ubuntu 22.04 (ROS2 Humble · Gazebo Harmonic · PX4)
OpenVINS on EuRoC — valid drift
EuRoC R(D) ablation + /vio/internals shot
Gazebo tunnel + GT · OpenVINS on sim
IB_deg outage-coverage plot (offline)
= ALL FOUR DP7 DELIVERABLES (floor locked)
FLOOR LOCKED
D + 3-class bound + R(D) in sim
kill-camera demo + breathing cockpit
C++ fork · full RAIM-slope (stretch)
FLOOR vs STRETCH
GUARANTEED (by 11 Jun)
OpenVINS on EuRoC + Gazebo → drift<1.5% → est-vs-GT → documented workspace. All 4 DP7 deliverables. High confidence.
LIVE DEMO (Python)
integrity_monitor on published covariance → trust light + breathing bound + kill-camera. Medium-high confidence.
STRETCH (presented, not bet)
C++ internals fork · full whitened-D · generalized-eigenvalue RAIM slope → derived + offline. Dashed = not on critical path.
“When the camera dies, our drift bound still covers the truth 95%+ — and we know within half a second.”
A.E.T.H.E.R · DP7 · FLIGHT-TEST REPORT AE-001 · pg 7/7